## Slide 1
Depth-aware Vessel Network Analysis Pipeline
(a) Brightfield
(b) Multi-color GT
(c) R channel
(d) B channel
(e) R-B dominance
(f) R skeleton
(g) B skeleton
(h) R+B overlay
(i) Single GT skel
(j) R bridged
(k) B bridged
(l) R+B combined
(m) Gap Bridging Process
Before (filtered)
Bridging
After (connected)
→
→
(n) Bridge Zoom Detail
B bridge #1
before
bridging
after
R bridge #2
R bridge #1
Red R skel Blue B skel Orange R bridge Teal B bridge Purple R+B overlap Magenta JN Yellow EP

## Slide 2
Tangent-guided Gap Bridging Algorithm
Step 1
Endpoint Detection
Find skeleton pixels with
neighbor count = 1
Step 2
Tangent Estimation
Trace back 10-20 px along
skeleton → compute direction
Step 3
Candidate Matching
EP pair distance < 80 px
cos(θ) > cos(60°)
vessel mask overlap ≥ 70%
Step 4
Bézier Interpolation
P(t) = (1-t)³P₁ + 3(1-t)²tC₁
+ 3(1-t)t²C₂ + t³P₂
C₁ = P₁ + 0.4d·t₁
Step 5
Score & Select
score = (cos₁+cos₂)/2
- d/dmax · 0.2
+ vessel_ratio · 0.2
Greedy: best-first, no reuse
Bridging Scheme
Before Bridging
t₁
t₂
gap
After Bridging
Bézier bridge
Bridge Examples
B bridge
R bridge
R bridge

## Slide 3
Vessel Network Quantification
(a) Single GT vs Multi GT (N=215, top 80%)
 | Length | EP | JN
Single GT | 1.00 | 1.00 | 1.00
Multi GT | 1.26 | 0.80 | 1.21
(b) Virtual Staining Models vs Multi GT
(c) Normalized Metrics (Multi GT = 1.0)
Model | Length | EP | JN
PBBDM | 0.95 | 0.93 | 0.78
LBBDM | 1.00 | 0.65 | 0.77
WGANGP | 0.80 | 0.88 | 0.48
Pix2pix | 0.81 | 0.83 | 0.42
LSGAN | 0.70 | 0.77 | 0.39
PBBDM achieves the closest match to GT across all multi-color depth metrics

## Slide 4
Multi-sample Depth-aware Skeleton Comparison
Skel R (bridged)
Skel B (bridged)
R+B Combined
1-19-716
9-15-512
16-18-716
18-19-512
1-16-512